## Slide 2
Network Layer:
Logical Addressing

## Slide 3: Addressing
In addition to physical address that identify individual devices, the internet requires an additional addressing convention :
An address that identifies the connection of a host to its network

## Slide 4
Each internet address consists of 4 bytes (32 bits); defining 3 fields
Class type
Net id
Host id
These parts are of varying length , depending on the class of the address

## Slide 5
IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.

## Slide 6
An IPv4 address is 32 bits long.
Note

## Slide 7
The IPv4 addresses are unique and universal.
Note

## Slide 8
The address space of IPv4 is 232 or 4,294,967,296.
Note

## Slide 9: Classes
5 different field-length patterns are in use, each defining a class of address
For ex,
Class A addresses are numerically the lowest
They use only 1-byte to identify class type and NetId, and leave 3-bytes available for HostId numbers
This means Class A networks can accommodate far more hosts than Class B or class c networks, which provide 2 and 1 byte hosted fields respectively.

## Slide 10
Class D is reserved for multicast addresses.
Multicasting allows copies of a datagram to be passed to a select group of hosts rather that to an individual host.
It is similar to broadcasting, where a packet is passes to all possible destinations .
However, multicasting allows transmissions to a selected subset
Class E addresses are reserved for future use.

## Slide 11
Dotted-decimal notation and binary notation for an IPv4 address

## Slide 12
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Let’s Solve

## Slide 13
Solution
We replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 14
Change the following IPv4 addresses from dotted-decimal notation to binary notation.

## Slide 15
Solution
We replace each decimal number with its binary equivalent

## Slide 16
Find the error, if any, in the following IPv4 addresses.

## Slide 17
Solution
There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 18
In classful addressing, the address space is divided into five classes:
A, B, C, D, and E.
Note

## Slide 20
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111

## Slide 21
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 22: NetId and HostId
Find the netid and the hosted for each address :
4.23.145.90
227.34.78.7
246.7.3.8
129.6.8.4
198.76.9.23

## Slide 23
4.23.145.90
Class A; Netid : 4 Hostid : 23.145.90
227.34.78.7
Class D, no Hostid or Netid
c. 246.7.3.8
Class E, no Hostid or Netid
d. 129.6.8.4
Class B Netid : 129.6 Hostid : 8.4
e. 198.76.9.23
Class C Netid : 198.76.9 Hostid : 23

## Slide 31
Number of blocks and block size in classful IPv4 addressing

## Slide 32
In classful addressing, a large part of the available addresses were wasted.
Note

## Slide 33: Network Addresses
Play a significant role in classful addressing
It is the first address in the block
It defines the network to the rest of the internet.
Router routes a packet based on the network address
Given the network address, we can find the class of the address, the block, and the range of the addresses in the block

## Slide 41: Mask
A mask is a 32-bit number that gives the first address in the block (the network address) when bitwise ANDed with an address in the block.

## Slide 44: Applying the masks
Applying mask to an unsubnetted network is simple
Two rules can help find the network address without applying the AND operation
If the mask byte is 255, retain the corresponding byte in the address
If the mast byte is 0, set the corresponding byte to 0

## Slide 47: Note :
Note that we must not apply the default mask of one class to an address belonging to another class

## Slide 48: CIDR Notation
The CIDR or classless inter domain routing, is used to explicitly indicate the default mask
In this notation, the number of 1s in the mask is added after a slash at the end of the address
For example, the address 18.46.74.10 which is class A address with the mask 255.0.0.0 is written as 18.46.74.10/8 to show that there are eight 1s in the mask.

## Slide 49
Similarly, the address 141.24.74.69 which is class B address with the mask 255.255.0.0 is written as 141.24.74.69/16 to show that there are sixteen 1s in the mask.
In the same way, the address 200.14.70.22 is written as 200.14.70.22/24
CIDR notation is particularly useful in classless addressing

## Slide 50: Address Depletion
Due to the classful addressing scheme and due to fast growth of internet, the available addresses are almost depleted.
We have run out of class A and B addresses, and a class C block is too small for most middle-size organizations
Solution is Subnetting and Supernetting

## Slide 51: Subnetting

## Slide 54: Addresses in a network with and without subnetting

## Slide 55: Hierarchy concept in telephone number

## Slide 59: The subnetwork address is 200.45.32.0

## Slide 60: Number of Subnetworks
The number of subnetworks can be found by counting the extra 1s that are added to the default mask to make the subnet mask
For Ex: The no of extra 1s is 3; therefore the number of subnets is (23 = 8).

## Slide 61: Number of addresses per subnet
The number of addresses per subnetwork can be found by counting the number of 0s in the subnet mask
For ex: the number of 0s is 13; therefore the number of possible addresses in each subnet is 213 = 8192.

## Slide 63: Supernetting
Class A and B addresses are getting depleted
Class C addresses are still available
However, the size of a class C block with a mx number of 256 addresses may not satisfy the needs of an organization
Even a mid size organization may need more addresses
One solution is Supernetting

## Slide 64: Contd…
In supernetting, an organization can combine several class C blocks to create a large range of addresses
For Ex : An organization that needs 1000 addresses can be granted four class C blocks.
The organization can then use these addresses in one super network as shown

## Slide 65: A Supernetwork

## Slide 67: Subnet vs Supernet mask
A subnet mask that divides a block into 8 sub blocks has three more 1s (23= 8) than the default mask;
A supernet mask that combines eight blocks into one superblock has three less 1s than the default mask

## Slide 68: Comparison of subnet, default, and supernet mask

## Slide 69: CIDR notation
This notation can also be used when we have supernets
For eg: the notation 141.14.192.3/24 shows a class C address, but the address
141.14.192.3/21 shows that the address
belongs to the supernet with the mask
255.255.248.0

## Slide 70
Classful addressing, which is almost obsolete, is replaced with classless addressing.
Note